## Slide 1: TUTORIAL TIME-SYNCHRONIZED STATE ESTIMATION IN MICRO-PMU UNOBSERVABLE DISTRIBUTION SYSTEMS
Anamitra Pal
May 2024

## Slide 2: Content
Introduction
Bayesian estimation
Sensor placement as a feature selection problem
Deep learning-based distribution system state estimation (DNN-based DSSE)
Data generation – MATLAB-OpenDSS
DNN training – Python-Keras
Results

## Slide 3: Introduction
Why do we need to do DSSE based on µPMU measurements?
System states are varying more frequently due to increasing penetration of distributed energy resources
Why do we need to do μPMU placement for incompletely observed systems?
It is economically not viable to have complete observability by μPMUs. DNN-based DSSE is proposed as a strategy to overcome the unobservability problem

## Slide 4
Conventional state estimation problem
: measurement vector
: state vector
: random noise
Basic requirements for closed form solution
Physical equations that relate and are known
What if ?
Closed form solution!
Let us treat and as random variables
Bayesian state estimation problem
Minimum mean squared estimator
Basic requirement for closed form solution
Knowledge of
Is the integration easy?
Yes
No
Deep learning!
No
Closed form solution!
Yes
Bayesian State Estimation
Estimation in presence of severe rank deficiency

## Slide 5
Distribution Learning from Load Data
Online Implementation
Topology Estimates
Slow Timescale Data
Distribution Estimate
Real-Time PMU/micro-PMU Measurements
State Estimates
Trained DNN-TI
Trained DNN-SE
DNN-TI for Topology Identification (Classification)
Training samples
DNN-SE for State Estimation (Regression)
Monte Carlo Sampling
Training Data Generation
Injection samples
Power flow
Measurement Noise Addition
Offline Learning
PMU/micro-PMU Placement

## Slide 6
Distribution Learning from Load Data
Online Implementation
Slow Timescale Data
Distribution Estimate
Real-Time µPMU Measurements
State Estimates
Trained DNN-SE
Training samples
DNN-SE for State Estimation (Regression)
Monte Carlo Sampling
Training Data Generation
Injection samples
Power flow
Measurement Noise Addition
Offline Learning
µPMU placement

## Slide 7: Schematic of the Proposed Method
Online Implementation
Real-Time PMU/micro-PMU Measurements
State Estimates
Trained DNN-SE
No
DNN-SE for State Estimation (Regression)
Monte Carlo Sampling
Training Data Generation
load/generation samples
Power flow
Measurement Noise Addition
Power flow
Measurement Noise Addition
Offline Learning
Distribution Learning from load/generation data
Yes
Fitted distribution using KDE
PMU/micro-PMU Placement
Slow time scale historical smart meter measurements
Is the number of samples enough?

## Slide 8
Smart Meter
15-minute average power (kw)
measurements are not available in real-time
120 samples/second voltage phasor
real-time measurements
µPMU
Smart meter data is only used to generate sample voltage phasors to train neural network (Offline operation)
Real-time µPMU measurements is used in testing stage (Online operation)
Two-sample Kolmogorov–Smirnov test
Shape
Mann Whitney U Test
Median
Can we use Kernel Density Estimation (KDE) to create high resolution power injection samples from historical smart meter data
Different Time Resolution

## Slide 9
DNN based DSSE
Regression
Spearman’s Correlation Coefficient
Numerical input Numerical output
Feature Selection
Used for DNN
Finds the minimum number of required µPMUs for incompletely observed networks
Integrated µPMU Placement
µPMU Placement for Incompletely Observed Networks

## Slide 10
DNN Training
# of layers
# of neurons
Activation function
Loss function
Batch size
Optimizer
Learning rate
Reduce on plateau
Dropout
Batch normalization
Grid search
Sensitivity analysis
DNN Training

## Slide 11
DNN-based DSSE for unbalanced three phase systems with interphase correlations
DNN Training

## Slide 12: Creating High Resolution Load Profiles for Primary Network
6-8 loads to each transformer
10,000 Monte Carlo runs for different combinations of loads (25 loads are available from Pecan street data)

## Slide 13
IEEE 34-Node System

## Slide 14
Historical energy readings can be used to generate instantaneous high speed power injections for scenario generation using KDE
µPMU placement ensures acceptable accuracy for DNN-based DSSE
Summary

## Slide 15
Journal
B. Azimian, R. S. Biswas, S. Moshtagh, A. Pal, L. Tong and G. Dasarathy, "State and Topology Estimation for Unobservable Distribution Systems Using Deep Neural Networks," in IEEE Transactions on Instrumentation and Measurement, vol. 71, pp. 1-14.
B. Azimian, S. Moshtagh, A. Pal and S. Ma, "Analytical Verification of Performance of Deep Neural Network Based Time-Synchronized Distribution System State Estimation," in Journal of Modern Power Systems and Clean Energy.
A. C. Varghese, H. Shah, B. Azimian, A. Pal and E. Farantatos, "Deep Neural Network-Based State Estimator for Transmission System Considering Practical Implementation Challenges," in Journal of Modern Power Systems and Clean Energy.
Conference
R. S. Biswas, B. Azimian and A. Pal, "A Micro-PMU Placement Scheme for Distribution Systems Considering Practical Constraints," 2020 IEEE Power & Energy Society General Meeting (PESGM), Montreal, QC, Canada, 2020, pp. 1-5.
B. Azimian, R. S. Biswas, A. Pal and L. Tong, "Time Synchronized State Estimation for Incompletely Observed Distribution Systems Using Deep Learning Considering Realistic Measurement Noise," 2021 IEEE Power & Energy Society General Meeting (PESGM), Washington, DC, USA, 2021, pp. 1-5.
B. Azimian, A. Pal, B. Abu-Jaradeh, L. Chen and P. Markham, "PMU-Timescale Topology Identification of Sub-station Node-Breaker Models using Deep Learning," 2023 IEEE Power & Energy Society General Meeting (PESGM), Orlando, FL, USA, 2023, pp. 1-5.
S. Moshtagh, A. I. Sifat, B. Azimian and A. Pal, "Time-Synchronized State Estimation Using Graph Neural Networks in Presence of Topology Changes," 2023 North American Power Symposium (NAPS), Asheville, NC, USA, 2023, pp. 1-6.
Book Chapter
B. Azimian, R. S. Biswas, and A. Pal, “Application of AI and machine learning algorithms in power system state estimation.” in “Cyber-physical power systems: challenges and solutions by AI/ML, big data, blockchain, IoT, and information theory paradigms”, Wiley-IEEE Press, Ch. 23, 2023.
Publications

## Slide 16
Thank you!